## Slide 1: Laser Induction
Version: 9
Last updated: 28 Feb 2023
Ruby version: 2.3.1.24878
This presentation is available on the Laser PC in Desktop / Laser induction

## Slide 2: Agenda
Personal intros, experiences and expectations
Intro to the laser
Health & Safety
Machine maintenance
Access to the space and machine booking
Materials shop
Workflow
Knowledge gaps and next steps
Register account on Ruby

## Slide 3: Intro to the laser
Laser, mirrors, lens, gantry, bed (movable), rotary attachment
Cut and engrave through vaporisation of materials (and mark metal)
Result is a combination of material, laser power and speed and the properties of the design
CO2 laser capabilities
Master resource: Tools page

## Slide 4: Laser, mirrors, lens, gantry, bed
Bed
Our laser is oriented the other way around (first and second mirror on the right), but the principle is the same.
Gantry

## Slide 5: CO2 laser capabilities
Cut & engrave results depend on:
Material (its reaction to laser light)
Power
Speed
DPI (engraving?) / Frequency
Passes (repeat cuts)
Condition of the machine
Age of laser tube
Size of bed

## Slide 6: Health & Safety
No unattended use
Danger of death - permitted materials only
Do not override the safety mechanisms
Do not use if you haven’t been inducted



## Slide 7: Machine maintenance
The laser machine is generally in really good working order
This is due to maintenance before and after each use, and regular maintenance by the lasertechs
A dirty machine performs sub optimally
Accumulated dirt can cause corrosion and other damage
Please report problems on discourse and tag @lasertechs

## Slide 8: High-level workflow
1. Preparation
  Files / Materials / Booking
2. Startup
  Cleaning, safety review
  Power, material placement and focus
3. Run job
  Ruby: Manage > Design > Prepare > Produce
4. Cleanup and shut down

## Slide 9:  Preparation
Doesn’t have to be done in the Makerspace
2D file in the appropriate format
  Adobe Illustrator, Inkscape (cut and vector engrave)
  JPG and other formats (engrave)
Materials
  Purchase material – must be laser-safe
  Shop stock – stock levels not guaranteed

## Slide 10:  Preparation
Book a session
  Host vs non-host
  Procedure
Make sure you have your Ruby password!

## Slide 11:  Startup
Power
  Laser PC on
  Tap tool control with fob
  Laser on
  Wait for warmup and homing

## Slide 12:  Startup
Honeycomb bed
  Clear out any bits left on the bed (brush / remove and vacuum)
  Make sure it is firmly seated on rails

## Slide 13:  Startup
Prepare to clean
  Move the bed to a comfortable height
  Move the head to a comfortable position
  Place a blue paper towel sheet and cleaning supplies on the bed

## Slide 14:  Startup
Nozzle
  Inspect:
    Unscrew – clockwise when seen from above
    A dirty nozzle is a good indication that other parts will need cleaning
  If dirty:
    Use spray foam and a cotton bud
    Replace finger-tight
Tip: Turn the laser on and move it to a convenient
location for accessing the head. You can also lower
bed if that helps.

## Slide 15:  Startup
3rd mirror
  Inspect:
    Hold mirror in one hand, unscrew thumbscrews with the other
    Carefully lift mirror and inspect it for dirt
  If dirty:
    Note orientation when removing
    Puff, douse with lens cleaning fluid, dab with lens tissue
    Return and tighten screws quite tightly

## Slide 16:  Startup
Lens
  Inspect:
    Hold lens tray in one hand, unscrew with the other – clockwise when seen from above
    Slide lens out
    Hold lens to the light and inspect it for dirt (scratches and burnt spot are OK)
  If dirty:
    Puff, douse one side with lens cleaning fluid, wait 30 seconds, dab with lens tissue (using each part of the tissue only once)
    Repeat on the other side
    Return and tighten finger-tight
If the lens is milky, do not use. Report to @lasertechs

## Slide 17
Watch videos

## Slide 18:  Startup
Safety
  Are you using laser-safe material (see Tool page)?
  Is there a CO2 fire extinguisher nearby?
  Note the Emergency Stop button

## Slide 19:  Startup
Material placement and focus
  Place within comfortable reach (you’ll need to be able check that the material is square on the bed)
  Double buttons to raise and autofocus bed
  Roughly position head over material
  Use the focus stick to fine-tune the focus

## Slide 20:  Run job
Open Ruby from the Start Menu
Login to Ruby
Manage – access previous designs and jobs
Design – import a new design
Prepare – apply specific laser settings
Produce – cut and engrave
A brief intro to Ruby follows…

## Slide 21: Intro to Ruby
Ruby is a Laser Control Software specific to Trotec lasers
It is approximately equivalent to LightBurn, RDWorks, etc
It is a replacement for JobControl
You do everything (except the design) in Ruby
Each user needs a login to access Ruby
The software is web based (runs in the browser)
“Designs” are files
“Jobs” are designs + cut and engrave settings (repeat work)

## Slide 22: 1. Get started

## Slide 23: 2. Manage
View your previous designs and jobs

## Slide 24: 3. Design
Don’t bother to design here – the tools are rudimentary
Just import your files

## Slide 25: 4. Prepare
Position it on the bed
Set the material and output settings
Set/tweak the colours to determine which output settings apply to each object

## Slide 26: 5. Produce
Cut and engrave
Wait before opening the lid to let smoke clear
Hold material so it doesn’t move
Tap pieces to make sure that they are cut through

## Slide 27:  Cleanup and shut down
Remove any debris from the bed
Check (and clean) the nozzle, mirror, lens
Shut down the laser
Logout of Ruby
Shut down the PC
Sign out of the tool control
Clear junk bits
Place usable offcuts in the scrap bin

## Slide 28: Ruby “remote” access
Use this to learn, or to set up your job
You must be at the Makerspace!
Login to the Makerspace wifi
Go to https://slms-05.local:2402/
You can do everything except start the laser!
Go to the laser PC and login to start the job
Note: You can only be logged in one PC at a time

## Slide 29: Rotary attachment

## Slide 30: Help
Trotec manuals - https://www.rubyhelp.com/
SLMS wiki – loads more detail than in this presentation

## Slide 31: Knowledge gaps and next steps
2D design
Understanding materials and their interactions with the laser
Advanced techniques
Job optimisation
Workshops and “project days”
First project

## Slide 32: Resources to explore
Brendon’s book
  https://lasercuttingfundamentals.info/
Vecteezy – vector stock images (not all laser-friendly)
  https://www.vecteezy.com/
Box generator – parametric, lots of designs
  https://www.festi.info/boxes.py/
Laser-ready designs – download and cut!
  https://designbundles.net/craft/laser-cutting-designs
  https://www.librarylaser.com/en/

## Slide 33: Ruby registration
Lasertechs, follow the instructions here
(Look for the heading - 6. User administration)
Each user needs a username associated with an email address and a password.
There is no “forgot password” feature.
If you forget your password, contact the lasertechs on discourse.